## Slide 1: Fault-Tolerant Architecture Design for Flow-Based Biochips
Morten Chabert Eskesen

## Slide 2: Flow-Based Biochips
Can run biochemical applications
  Microreaction Technology
  Cell Biology
  Diagnosis Testing
  Basic building block

## Slide 3: Outline
  Components
  Faults, Causes and Fault Modeling
  Component Library Extension
    Fault-tolerant components
  Problem Formulation
  Motivational Example
  Architecture Evaluation
  Architecture Synthesis
    Design Transformations
  Proposed Solutions
  Experimental Evaluation
  Conclusions

## Slide 4: Components
Valves combine to form more complex units
Microfluidic Switch
Microfluidic Mixer

## Slide 5: Video of Mixer
Microfluidic Mixer
http://groups.csail.mit.edu/cag/biostream/

## Slide 6: Faults, Causes and Fault Modeling
Block (a)-(c)
Leak (d)-(f)
  Partial leak (g)-(h)
Misalignment (i)
Faulty pumps
Degradation of valves
Dimensional errors

## Slide 7: Component Library - Extension
Switch
Mixer
Heater
Detector
Filter
Separator

## Slide 8: Problem Formulation
Given
  A netlist (components and their interconnections)
  A component library L
  An application graph G with a deadline
  A fault model Z
Determine
  A fault-tolerant netlist
Such that
  The biochip is fault-tolerant and
  It minimises the cost of the architecture

## Slide 9: Motivational Example - Setup
  Initial architecture
  Application Graph

## Slide 10: Motivational Example - Solution
Straightforward solution
  Redundant components
  Cost: 129
Optimised solution
  Fault-tolerant components
  Cost: 96

## Slide 11: Architecture Evaluation
Fault scenario generation
  Each iteration
    Applies a fault scenario
    Determines connectivity
    Finish time, δ, of the application
Channel S1 → Mixer1 is blocked, Channel of Heater1 suffers from a block defect.
A valve in the pump of Mixer1 and the valves controlling the channel towards S3 and the channel towards S5 of S4 are stuck open
Connectivity
  1 if connected, 0 otherwise
  Determined by Breadth First Search
  Considers blocked route and valve faults on switches
Scheduling
  Maximum of 0 or δ - application deadline
  Determined by List Scheduling
  Routes determined by Breadth First Search
Physical constraints
  Sum of
    Total number of valves
    Total number of connections

## Slide 12: Architecture Synthesis
Two metaheuristics:
  Simulated Annealing
  GRASP

## Slide 13: Design Transformations
Add redundant component
Make component fault-tolerant
Add redundant connection
Remove redundant component
Make component non fault-tolerant
Remove redundant connection

## Slide 14: Greedily Randomized Adaptive Search Procedure
Two phases
  Construction phase
  Local search phase
Candidate list
Ranking of components
RCL
Moves

## Slide 15: Methodology
Steps in the methodology:
Architecture design
Fault-tolerant architecture synthesis
  Considering an application and a fault model
Physical architecture synthesis
Fabrication
Testing
  If a fault is present and not in the fault model or it is not tolerated, discard the chip
  Or if the application is not schedulable, the chip is discarded

## Slide 16: Experimental Evaluation
Objective function evaluation
Initial features of benchmarks
The resulting netlists of the benchmarks

## Slide 17: Experimental Evaluation
Yield evaluation
Initial features of benchmarks
Only benchmark S-1 used and GRASP was the algorithm
The result of yield evaluation

## Slide 18: Conclusions
Extended the component library with fault-tolerant components
Proposed a fault-model for flow-based biochips
Synthesising a fault-tolerant architecture
Both algorithms produce fault-tolerant netlists for all benchmarks
  GRASP provided better results in terms of solution quality and performance
The yield evaluation proved that even generating a fraction of the possible fault scenario can lead to good fault-tolerance on all fault scenarios

## Slide 19: Simulated Annealing
Initial solution
Solution acceptance
Temperature cooling
Moves

## Slide 20: Class Diagram