## Slide 1: Analysis Methods for Mixed-Criticality Applications on TTEthernet-based Distributed Architectures
Sorin Ovidiu Marinescu
Technical University of Denmark

## Slide 2: Outline
Motivation
Partitioned Architectures
  At CPU-level
    IMA Analysis
  At network level
    TTEthernet
    TTEthernet Analysis and Simulation
    Trajectory Approach Applied to TTEthernet
Conclusions

## Slide 3: Motivation
Federated Architecture
Real time applications implemented using distributed systems
PE
Application A 1
Application A 2
Application A 3
Mixed-criticality applications share the same architecture
SIL3
SIL3
SIL4
SIL4
SIL4
SIL1
SIL2
SIL1
Solution: partitioned architecture
Integrated Architecture

## Slide 4: Partitioned Architectures – CPU level
Spatial partitioning
      protects one application’s memory
      and access to resources from another
      application
Temporal partitioning
      partitions the CPU time among applications

## Slide 5: System model
Spatial and temporal partitioning scheme similar to IMA (Integrated Modular Avionics)
Applications are allowed to execute only within their assigned partitions.
Each partition can have its own scheduling policy.

## Slide 6: Problem formulation
Given
    A set of mixed-criticality applications
    A set of processing elements (PEs)
    The mappings of tasks to the PEs
    The assignments of tasks to partitions
    The size of the Major Frame and of the System Cycle
Determine
    The worst-case response times of tasks scheduled in partitions using fixed-priority preemptive scheduling
Two schedulability analysis methods compared
    SA – existing IMA analysis
    SA+ - our proposed method, an extension of WCDOPS+ to consider IMA

## Slide 7: Motivational example

## Slide 8: SA (Audsley and Wellings)
Schedulability analysis for FPS tasks on IMA architectures
Tasks are independent and for every task τi :
Start times of partition slices within a Major Frame are periodic.
When analyzing a task in a partition, the other time-partitions are merged together into a “higher priority task”

## Slide 9: SA (Audsley and Wellings)
Schedulability analysis for FPS tasks on IMA architectures
Tasks are independent and for every task τi :
Start times of partition slices within a Major Frame are periodic.
When analyzing a task in a partition, the other time-partitions are merged together into a “higher priority task”

## Slide 10: SA+ (extended WCDOPS+)
WCDOPS+ - response time analysis algorithm for FPS tasks disposed in tree shaped transactions.
WCDOPS+ was extended to take into account the partitions.
The concepts of availability and demand were introduced.
SA+ does not assume that the partition slices have to be periodic within a Major Frame.

## Slide 11: Availability and demand
The availability associated to a task τi during a time interval t is equal to the processor time that is not used by other partitions during t.
The demand for a task τi during a time interval t is equal to the sum of the processor times required by τi and all higher priority tasks mapped to the same processor during t.

## Slide 12: Extended completion time

## Slide 13: Experimental results
Benchmarks:
  7 synthetic
  1 real-life test case from E3S
Our method provides less pessimistic worst-case response times
Notes: To make more concise!

## Slide 14: Partitioned Architectures – network level
TTEthernet is very well suited for mixed-criticality applications
Traffic classes:
  synchronized communication
    Time Triggered (TT) - based on static schedule tables
  unsynchronized communication
    Rate Constrained (RC) – ARINC 664p7 traffic class
    Best Effort (BE) – no timing guarantees
ARINC 664p7 compliant
Standardized as SAE AS 6802
Notes: When talking about traffic classes, also mention integration policies:
timely block – the transmission of an RC frame is postponed if it will not terminate before the transmission of a scheduled TT frame
pre-emption – the transmission of an RC frame is pre-empted if a TT frame is scheduled for tranmission
shuffling – if an RC frame is transmitting, the TT frame will be sent only after the transmission finished

## Slide 15: TTEthernet network
Full-Duplex Ethernet-based data network for safety-critical applications composed of clusters
Each cluster has a clock synchronization domain
Inter-cluster communication using RC traffic
ES1
ES2
SW1
ES3
ES4
ES5
ES6
SW2
ES7
ES8
Cluster 1
Cluster 2

## Slide 16: Separation at network level
ES1
ES2
SW1
SW2
ES3
ES4
Full-Duplex Ethernet-based data network for safety-critical applications
End System
Network Switch

## Slide 17: Separation at network level
SW1
SW2
vl2
vl1
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
virtual link
Notes: The Ethernet protocol does not offer separation between messages of different criticalities. ARINC 664p7 manages this through the concept of Virtual Links, by emulating point-to-point connectivity over the network. The virtual link is defined as the “logical unidirectional connection from one source system to one or more destination end systems”. Thus the virtual link is a directed tree, with the sender as a root, and the receivers as leaf. Each virtual link is composed of a set of dataflow paths, one such dataflow path for each root-leaf connection.
One virtual link is assigned to one message only.
By using virtual links, the highly critical message m1 is separated from the non-critical message m2.
Let’s assume we have 2 applications, A1 and A2.

## Slide 18: Separation at network level
SW1
SW2
dp1
vl1
dp2
l1
l2
l3
l4
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
dataflow path
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
dataflow link
Notes: Each virtual link is composed of a set of dataflow paths, one such dataflow path for each root-leaf connection.

## Slide 19: Separation at network level
Spatial separation
  achieved through virtual links
Temporal separation
  enforced by schedule tables for TT traffic and bandwidth allocation for RC traffic
Contention problems
  how is the TT and RC traffic integrated?
    preemption
    shuffling
    timely block
Notes: Let’s recapitulate why is TTEthernet suitable for mixed-criticality applications? Mixed-criticality messages need to be separated spatially and temporally. And TTEthernet provides mechanism for that. Spatial separation is achieved…

## Slide 20: Dataflow integration
ES1
ES2
SW1
ES3
vl3
vl1
vl2
tt1 – TT frame
rc1 – RC frame

## Slide 21: TT Transmission
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT
b

## Slide 22: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 23: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 24: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 25: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 26: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 27: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 28: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 29: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
NS2
NS3
FU
TTR
B1,Tx
B2,Tx
TTS
NS1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 30: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
NS2
NS3
FU
TTR
B1,Tx
B2,Tx
TTS
NS1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 31: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 32: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 33: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 34: TT Transmission
b
b
CPU
P1,1
τ1
P1,2
τ2
B2,Tx
B1,Tx
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
TT
a
c
d
e
f
g
h
i
j
k
l
m
SR
SS
a
c
d
e
f
g
h
i
j
k
l
m
Packing message m2 into frame f2
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
TTS sends f2 to NS1
f2 is sent on the dataflow link to NS1
The Filtering Unit (FU) checks the frame f2
Expected receive time specified in receive schedule SR
TTR checks if f2 arrives according to schedule
Place f2 in buffer B1,Tx for transmission
Send time specified in send schedule SS
FU checks f2
Store the frame into receive buffer B2,Rx
Task τ4 reads f2 from buffer
b
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 35: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 36: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 37: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 38: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 39: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
Send f1 when there is no TT traffic
FU checks f1
Copy to receiving Q2,Rx
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT
10
11
12
13

## Slide 40: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 41: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 42: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 43: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 44: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 45: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 46: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 47: RC Transmission
CPU
P1,1
τ1
P1,2
τ2
Q1,Tx
Q2,Tx
B2,Tx
B1,Tx
TR2
TR1
RCS
TTS
P1,3
P2,1
τ4
P2,2
τ3
P2,3
CPU
FU
Q1,Rx
Q2,Rx
B1,Rx
B2,Rx
ES1
ES2
SW2
SW3
FU
TP
TTR
B1,Tx
B2,Tx
TTS
SW1
SS
f2
f3
f4
f1
RC
TT
QTx
1
2
3
4
5
6
7
8
9
10
11
12
13
SR
SS
1
Packing message m1 into frame f1
2
Insert it in queue Q1,Tx
3
Traffic Regulator (TR) ensures bandwidth for each VL
4
RC scheduler RC multiplexes frames coming from TRs
5
TTS transmits f1 when there is no TT traffic
6
f1 is sent on the dataflow link to NS1
7
FU checks the validity of the frame
8
Traffic Policing (TP) checks that f1 arrives
according to the BAG
9
Copy f1 to outgoing queue QTx
10
Send f1 when there is no TT traffic
11
FU checks f1
12
Copy to receiving Q2,Rx
13
Task τ3 reads f1 from the queue
A1: τ1 à m1 à τ3, RC
A2: τ2 à m2 à τ4, TT

## Slide 48: Problem formulation
Given
    The network topology G
    The set of TT and RC frames (FTT and FRC)
    The TT schedule tables
    The set of virtual links
    The assignment of frames to virtual links
    For each frame the size, the deadline and the period/rate
    The size of the application cycle Tcycle
Determine
    The worst-case end-to-end delays of the RC frames
Two worst-case end-to-end analyses for RC traffic compared
    The analysis proposed by Steiner (2011)
    Our TTEthernet simulator

## Slide 49: Steiner’s Analysis
Schedule porosity is obtained by:
  TT slots of length lTT alternated with blank slots of length lblank for RC
Max. backlog: the difference between max. ingress dataflow and the egress dataflow
Is pessimistic:
    does not ignore frames that already delayed a RC frame on a previous link
    assumes the lblank intervals are uniformly distributed
vx
k
vy
[vx, k]
[k, vy]

## Slide 50: RC Frame End-to-End Delay Analysis
Before being sent of a dataflow link, a RC frame can be delayed by:
  scheduled TT frames
  queued RC frames
  technical latency
  policy specific

## Slide 51: RC Frame End-to-End Analysis
ES1
SW2
SW1
ES2
vl3
vl2
vl1
SW3
vl4
SW2 → SW1
f3,1
0
100
200
300
400
500
600
f4,1
SW3 → SW1
SW1 → ES2
f2,1
ES1 → SW1
f1,1
f2,1
f4,1
f1,1
f3,1
C
[SW1, ES2]
f1
QTT
[SW1, ES2]
QRC
[SW1, ES2]
QTL
SW1
R
f1
f3,1
f2, f4– TT frames
f1, f3 – RC frames

## Slide 52: TTEthernet simulator
RC traffic is simulated based on the given network arch. and known TT static schedules
1 TTEthernet cluster, 1 clock synchronization domain
RC traffic is asynchronous
  we assigned random arrival times to the RC frame instances at their source end-systems
The obtained worst-case end-to-end delays are not exact
  we can’t say that a RC frame is schedulable, but we may find out that it’s not

## Slide 53: Experimental results
11 synthetic benchmarks from [TSP12]
[TSP12] Domitian Tamas-Selicean and Paul Pop. Synthesis of communication schedules for TTEthernet-based mixed-criticality systems. In Proceedings of the International Conference on Hardware/Software Codesign and System Synthesis, 2012.

## Slide 54: End-to-End Delay Analysis Methods
Network Calculus
Trajectory approach
  Set of sporadic flows – each flow follows a static path Pi
    Ti – minimum inter-arrival time
    Pi – static priority
    – processing time on node h
    Di – maximum acceptable end-to-end delay
    Ji – maximum release jitter
  Packet scheduling is non-preemptive

## Slide 55: Trajectory Approach Principle
Once a packet started to be processed on the last node of its trajectory it can not be interrupted
It makes sense then to determine “only” the latest starting time on the last node in the trajectory
Move backwards through the sequence of visited nodes
Identify the preceding packets and busy periods that ultimately affect the delay of m (the packet under study)

## Slide 56: Trajectory Approach Applied to AFDX
The AFDX configuration on which trajectory approach is applied:
AFDX virtual link paths define trajectory approach flows
The flows have the same static priority, same Ti

## Slide 57: Trajectory Approach Applied to AFDX
The equivalent trajectory approach system:

## Slide 58: Example Scheduling of Packets
We are interested in the starting time of packet 4 on node SW3-ES6

## Slide 59: Trajectory Approach Applied to TTEthernet
The TT and RC frames are modeled as trajectory approach flows
TTEthernet TT frames offsets
How is the trajectory approach applied to TTEthernet depends on the TT/RC integration policy
  Shuffling
    FP/FIFO non-preemptive scheduling policy
  Timely block and preemption
    FP/FIFO scheduling of packets
    Trajectory approach needs to be extended to permit preemption

## Slide 60: End-to-End Delay Components
The components of the latest starting time of packet m on its last visited node q are:
  – the delay caused by the packets having a priority higher or equal to m
  – the delay directly due to non-preemption
  – the maximum network delay

## Slide 61: Allowing preemption
The generation interval for packets with higher or equal priority than m

## Slide 62: Allowing preemption
The generation interval for packets with higher or equal priority than m when preemption is allowed

## Slide 63: Future work
A holistic analysis to integrate our analyses done at the CPU-level and at the network level
Optimal design of virtual links
Study of the influence of different frame parameters on the end-to-end delays
Multi-cluster TTEthernet networks
Notes: To make more concise!

## Slide 64: Conclusions
Functions with different criticalities can share the same computing platform only if there is enough spatial and temporal separation between them
Separation at CPU-level achieved through an IMA-like partitioning
Schedulability analysis of FPS tasks that takes into account the partitions
We have extended a state-of-the-art RTA algorithm to consider a non-periodic partitioning system
Notes: To make more concise!

## Slide 65: Conclusions
Separation at network level provided by TTEthernet
  Predictability is achieved using three classes of traffic: TT, RC and BE
  Spatial separation is achieved trough virtual links
  Temporal separation is enforced by schedule tables for TT traffic and bandwidth allocation for RC traffic
End-to-end delay analysis of RC messages
  We compared the results obtained by the previously proposed TTEthernet analysis and by our TTEthernet simulator
  We proposed an extension of the trajectory approach
Analysis tools are needed to support the designer in order to obtain schedulable implementation of mixed-criticality applications on partitioned architectures
Notes: To make more concise!