## Slide 1: Analysis and Optimization of Mixed-Criticality Applications on Partitioned Distributed Architectures
Domițian Tămaș-Selicean, Sorin Ovidiu Marinescu and Paul Pop
Technical University of Denmark

## Slide 2: Outline
Motivation
Separation of mixed-criticality applications
  At processing element level
  At communication level
Problem formulation and example
Optimization strategy
Experimental results
Conclusions

## Slide 3: Motivation
Safety is the property of a system that will not endanger human life or the environment
A safety-related system needs to be certified
A Safety Integrity Level (SIL) is assigned to each safety related function, depending on the required level of risk reduction
There are 4 SILs:
  SIL4 (most critical)
  SIL1 (least critical)
  SIL0 (non-critical) – not covered by standards
SILs dictate the development process and certification procedures

## Slide 4: Motivation
Federated Architecture
Real time applications implemented using distributed systems
PE
Application A 1
Application A 2
Application A 3
Mixed-criticality applications share the same architecture
SIL3
SIL3
SIL4
SIL4
SIL4
SIL1
SIL2
SIL1
Solution: partitioned architecture
Integrated Architecture

## Slide 5: Separation at PE-level
Partition = virtual dedicated machine
Partitioned architecture
  Spatial partitioning
    protects one application’s memory and access to resources from another application
  Temporal partitioning
    partitions the CPU time among applications

## Slide 6: Separation at PE-level
Temporal partitioning
  Static partition table
    Repeated with a period MF
    Partition switch overhead
    Each partition can have its own scheduling policy
    A partition has a certain SIL
Partition
Partition
slice
Major Frame
PE 1
PE 2
PE 3
PE 1
PE 2
PE 3
Problem: optimize task mapping
and allocation of partitions

## Slide 7: Separation at Network-level
ES1
ES2
NS1
NS2
ES3
ES4
Full-Duplex Ethernet-based data network for safety-critical applications
Compliant with ARINC 664p7 “Aircraft Data Network”
End System
Network Switch
Notes: ARINC 664 p7 specifies a full-duplex Ethernet network for aircraft data networks.
It is composed of End – Systems connected by Network Switches and physical connections.

## Slide 8: Separation at Network-level
NS1
NS2
vl2
vl1
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
virtual link
Notes: The Ethernet protocol does not offer separation between messages of different criticalities. ARINC 664p7 manages this through the concept of Virtual Links, by emulating point-to-point connectivity over the network. The virtual link is defined as the “logical unidirectional connection from one source system to one or more destination end systems”.
By using virtual links, the highly critical message m1 is separated from the non-critical message m2.
Let’s assume we have 2 applications

## Slide 9: Separation at Network-level
NS1
NS2
dp1
vl1
dp2
l1
l2
l3
l4
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
dataflow path
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
dataflow link

## Slide 10: TTEthernet
Traffic classes
  Time Triggered (TT)
    based on static schedule tables
  Rate Constrained (RC)
    deterministic unsynchronized communication
    ARINC 664p7 traffic
  Best Effort (BE)
    no timing guarantees provided

## Slide 11: Application Model
SCS apps transmit TT messages
FPS apps transmit RC messages

## Slide 12: Problem formulation
Given
    A set of applications
    The criticality level (or SIL) of each task
    A set of N processing elements (PEs) and topology of the network
    The set of TT and RC frames
    The set of virtual links
    The size of the Major Frame and of the Application Cycle
Determine
    The mapping of tasks to PEs
    The sequence and length of partition slices on each processor
    The assignment of tasks to partitions
    The schedule for all the tasks and TT frames in the system
Such that
    All applications meet their deadline
    The response times of the FPS tasks and RC frames is minimized

## Slide 13: Motivational Example 1
Mapping and partitioning optimization
Notes: Use the motivational example from Journal!

## Slide 14: Motivational Example 1

## Slide 15: Motivational Example 1

## Slide 16: Motivational Example 2
ES1
ES2
NS1
ES3
vl3
vl1
vl2
 | period (us) | deadline (us) | Ci (us) | M
f1 ∈ FRC | 300 | 300 | 75 | vl1
f2 ∈ FTT | 200 | 200 | 50 | vl2
f3 ∈ FTT | 300 | 300 | 50 | vl3
Optimization of TT message schedules

## Slide 17: Motivational Example 2
ES1
ES2
NS1
ES3
vl3
vl1
vl2
 | period (us) | deadline (us) | Ci (us) | M
f1 ∈ FRC | 300 | 300 | 75 | vl1
f2 ∈ FTT | 200 | 200 | 50 | vl2
f3 ∈ FTT | 300 | 300 | 50 | vl3
Initial TT schedule
Notes: We show how the TT schedule influences the worst-case end-to-end delay of an RC frame.

## Slide 18: Motivational Example 2
ES1
ES2
NS1
ES3
vl3
vl1
vl2
 | period (us) | deadline (us) | Ci (us) | M
f1 ∈ FRC | 300 | 300 | 75 | vl1
f2 ∈ FTT | 200 | 200 | 50 | vl2
f3 ∈ FTT | 300 | 300 | 50 | vl3
Optimized TT schedule
Notes: f3,2 is postponed from ES2->NS1  f1,1 can be sent earlier

## Slide 19: Optimization Strategy
Tabu Search meta-heuristic
  Task mapping and partition slice optimization (TO)
    Considering TT frame schedules fixed
  TT frame schedules optimization (TM)
    Considering the task mapping and partition slices fixed
Tabu Search
  Minimizes the cost function
  Explores the solution space using design transformations

## Slide 20: Optimization Strategy
Degree of schedulability
  Captures the difference between the worst-case response time and the deadline
Cost Function

## Slide 21: Optimization Strategy: Design Transformations
Partition slice moves
  resize partition slice
  swap two partition slices
  join two partition slices
  split partition slice into two
Task moves
  re-assign task to another partition

## Slide 22: Optimization Strategy: Design Transformations

## Slide 23: Optimization Strategy: Design Transformations

## Slide 24: Optimization Strategy: Design Transformations

## Slide 25: Optimization Strategy: Design Transformations

## Slide 26: Optimization Strategy: Design Transformations

## Slide 27: Optimization Strategy: Design Transformation
Task re-assignment move
  To another partition of the same application
  To a partition of another application
  To a newly created partition
  Empty partitions are deleted

## Slide 28: Optimization Strategy: Design Transformations
TT frame moves
  advance frame transmission time
  advance frame predecessors transmission time
  postpone frame transmission time
  postpone frame successors transmission time
RC frame moves
  reserve space for RC frame
  resize reserved space for RC frame
  remove reserved space for RC frame

## Slide 29: Frame Representation for Moves
ES1
ES2
NS1
NS2
ES3
ES4
vl1
f1,1
[ES1, NS1]
f1,1
[NS1, NS2]
f1,1
[NS1, NS2]
f1,1
[NS1, NS2]

## Slide 30: Design transformations: Postpone move

## Slide 31: Design transformations: Advance move

## Slide 32: Design transformations: Reserve space for RC

## Slide 33: Design transformations: Resize RC reserved space

## Slide 34: RC Frame End-to-End Analysis
On a dataflow link, a RC frame can be delayed by:
  scheduled TT frames
  queued RC frames
  technical latency
  policy specific:
    timely block
    pre-emption

## Slide 35: RC Frame End-to-End Analysis
ES1
NS2
NS1
ES4
vl3
vl2
vl1
NS3
NS2 → NS1
f3,j
0
100
200
300
400
500
600
f4,1
NS3 → NS1
NS1 → ES4
f2,1
ES1 → NS1
f1,i
f2,1
f4,1
f1,i
f3,j
C
[NS1, ES4]
f1
QTT
[NS1, ES4]
QRC
[NS1, ES4]
QTL
NS1
R
f1
vl4

## Slide 36: RC Frame End-to-End Analysis
Approaches for analysis of ARINC 644p7 network traffic:
  Network Calculus, (Boyer, 2008)
  Finite State Machine, (Saha, 2007)
  Timed Automata, (Adnan, 2010)
  Trajectory Approach, (Bauer, 2009)
We use the method proposed in (Steiner, 2011)
    it takes into account also the TT traffic
    it is pessimistic:
      does not ignore frames that already delayed a RC frame
      on a previous link
      assumes uniformly distributed intervals of equal length
      reserved for RC traffic

## Slide 37: Experimental Results: TO
Benchmarks
  5 synthetic
  2 real life test cases from E3S
TO compared to:
  Straightforward Solution for Tasks (SST)
    Simple partitioning scheme, each application Ai is allocated a total time proportional to the utilization of tasks of Ai on the processor they are mapped to

## Slide 38: Experimental Results: TO

## Slide 39: Experimental Results: TO

## Slide 40: Experimental Results: TM
Benchmarks
  7 synthetic
  1 real life test case based on the SAE Automotive benchmark
TM compared to:
  Straightforward Solution for Messages (SSM)
    Builds TT schedules with the goal to optimize the end-to-end response time of the TT frames without considering the RC traffic

## Slide 41: Experimental Results: TM

## Slide 42: Experimental Results: TM

## Slide 43: Experimental Results: TM

## Slide 44: Conclusions
Applications of different criticality levels can be integrated onto the same architecture only if there is enough separation:
  Separation at PE-level achieved with IMA.
  Separation at network-level using TTEthernet.
We proposed a Tabu Search based optimization of task mapping and allocation to partitions, and of time partitions.
Only by optimizing the implementation of the applications, taking into account the particularities of IMA and TTEthernet, are we able to support the designer in obtaining schedulable implementations.
Notes: To make more concise!