## Slide 1: Timing Analysis of Rate Constrained Traffic for the TTEthernet Communication Protocol
Domițian Tămaș-Selicean1, Paul Pop1 and Wilfried Steiner2
1Technical University of Denmark
2TTTech Computertechnik AG

## Slide 2: Motivation
Point-to-point connection
Real time applications implemented using distributed systems
PE
Application A 1 -- highly critical
Application A 2 -- critical
Application A 3 -- non-critical
Bus connection
Reduces wiring and weight
Mixed-criticality applications share the same network
Notes: Example of point-to-point connection is the ARINC 429 data transfer standard for avionics, with a transfer rate of up to 100 kbit/s.
One option would be an Ethernet-based network, since it can achieves speeds up to 1 Gbit/s. But Ethernet is known to be unsuitable for real-time or safety-critical applications, as it is inherently a non-deterministic network.

## Slide 3: ARINC 664 p7 “Aircraft Data Network”
ES1
ES2
NS1
NS2
ES3
ES4
Full-Duplex Ethernet-based data network for safety-critical applications
End System
Network Switch
Notes: ARINC 664 p7 specifies a full-duplex Ethernet network for aircraft data networks.
It is composed of End – Systems connected by Network Switches and physical connections.

## Slide 4: ARINC 664 p7 “Aircraft Data Network”
ES1
ES2
NS1
NS2
ES3
ES4
CPU
RAM
ROM
NIC
Notes: Each End Systems consists of a Processing Element PE, containing a CPU, a a RAM and non-volatile memory, and a Network Interface Card

## Slide 5: ARINC 664 p7 “Aircraft Data Network”
ES1
ES2
NS1
NS2
ES3
ES4
NS1 to ES1
ES1 to NS1
dataflow link
Notes: In half-duplex implementations, frame collision is unavoidable, leading to unbounded transmission times.
ARIC 664p7 is a full-duplex network, thus allows simultaneous communication in both directions, collisions-free.

## Slide 6: ARINC 664 p7 “Aircraft Data Network”
NS1
NS2
vl2
vl1
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
virtual link
Notes: The Ethernet protocol does not offer separation between messages of different criticalities. ARINC 664p7 manages this through the concept of Virtual Links, by emulating point-to-point connectivity over the network. The virtual link is defined as the “logical unidirectional connection from one source system to one or more destination end systems”. Thus the virtual link is a directed tree, with the sender as a root, and the receivers as leaf. Each virtual link is composed of a set of dataflow paths, one such dataflow path for each root-leaf connection.
One virtual link is assigned to one message only.
By using virtual links, the highly critical message m1 is separated from the non-critical message m2.
Let’s assume we have 2 applications, A1 and A2.

## Slide 7: ARINC 664 p7 “Aircraft Data Network”
NS1
NS2
dp1
vl1
dp2
l1
l2
l3
l4
ES1
τ1
ES2
τ4
ES3
τ2
τ5
ES4
τ3
dataflow path
Highly critical application A 1: τ1, τ2 and τ3
  τ1 sends message m1 to τ2 and τ3
Non-critical application A 2: τ4 and τ5
  τ4 sends message m2 to τ5
Notes: T1 of A1 sends m1 to T2 and T3 on vl1.
vl1 is composed of dataflow paths dp1 and dp2, where dp1 is connecting ES1 to ES3 and dp2 is connecting ES1 to ES4.

## Slide 8: ARINC 664 p7 “Aircraft Data Network”
Deterministic Event Triggered communication
Separation of traffic enforced through “bandwidth allocation”
Bandwidth Allocation Gap (BAG) – minimum time interval between two consecutive instances of a frame on a virtual link
fx,1
fx,2
BAGx
Maximum bandwidth assigned to virtual link vli
BW (vli) = fi .size/BAGi

## Slide 9: TTEthernet
ARINC 664p7 compliant
Traffic classes:
  synchronized communication
    Time Triggered (TT)
  unsynchronized communication
    Rate Constrained (RC) – ARINC 664p7 traffic class
    Best Effort (BE) – no timing guarantees
Standardized as SAE AS 6802
Marketed by TTTech Computertechnik AG
Implemented by Honeywell on the NASA Orion Constellation
Notes: When talking about traffic classes, also mention integration policies:
timely block – the transmission of an RC frame is postponed if it will not terminate before the transmission of a scheduled TT frame
pre-emption – the transmission of an RC frame is pre-empted if a TT frame is scheduled for tranmission
shuffling – if an RC frame is transmitting, the TT frame will be sent only after the transmission finished

## Slide 10: TTEthernet
Composed of clusters
Each cluster has a clock synchronization domain
Inter-cluster communication using RC traffic
ES1
ES2
NS1
ES3
ES4
ES5
ES6
NS2
ES7
ES8
Cluster 1
Cluster 2

## Slide 11: Motivation

## Slide 12: Motivation
Notes: Upper: how the related work computes the WCD, by adding the worst-case latencies on each dataflow link, resulting in unlikely cases.
Lower: the exact WCD for this scenario.

## Slide 13: Sources of delay
Delays from scheduled TT frames on dlj
Delays from other RC frames transmitted on dlj
TT and RC traffic integration-induced delays
Technical latencies introduced by the network nodes

## Slide 14: Busy Period
To compute the size:
  Demand
  Availability
Notes: Analysis based on busy period – the time interval [t_c^j, t^j] within which the RC frames arrived before f_x in the outgoing queue are transmitted.
! The size of the busy period depends on the number of frames arrived, and the number of frames depends on the size of the busy period.
To compute, use availability and demand, and compute iteratively until the

## Slide 15: Worst-case end-to-end delay
For each dataflow path dpi, the end-to-end delay is the time difference between start of the busy period on the first dl0 and the end of the busy period on the last dln
  The start of the busy period on dlj is obtained by subtracting from the end of the busy period on dlj-1 all the RC frames transmitted on both dlj and dlj-1
The longest delay among all the dpi is the WCD
Notes: As mentioned, the related work sums up the worst-case delays on each dataflow link a frame is transmitted on, leading to pessimistic results.

## Slide 16: Worst-case end-to-end delay
WCD: the longest end-to-end delay for all dpi
The end-to-end delay on dpi: tn – tc0
Consider only possible scenarios: tcj depends on tj-1
NS1
NS2
dp1
vl1
dp2
l1
l2
l3
l4
ES1
ES2
ES3
ES4
Notes: A VL can be composed of se veral DPs, so the worst-case end-to-end is the longest end-to-end delay among all DPs
The end-to-end delay on a DP = t^n – t_c^0.
We consider only possible scenarios, so we compute the bp on l2 based on when the bp on l1 finished.
Down side: to determine the WCD, we have to consider each time instant on l1 as the starting time.

## Slide 17: Example

## Slide 18: Example
Exact WCD:

## Slide 19: Experimental Results
3 synthetic benchmarks:
  12 ESes and 4 NSes, 20 TT and 26 RC
  10 ESes and 5 NSes, 58 TT and 51 RC
  35 ESes and 8 NSes, 91 TT and 81 RC
The analysis is compared to the analysis from:
  W. Steiner. Synthesis of Static Communication Schedules for Mixed- Criticality Systems. In Proceedings of the International Symposium on Object/Component/Service-Oriented Real-Time Distributed Computing Workshops, pages 11–18, 2011.

## Slide 20: Experimental Results

## Slide 21: Conclusions
TTEthernet is very well suited for mixed-criticality applications
  Predictability is achieved using three classes of traffic: TT, RC and BE
  Spatial separation is achieved trough virtual links
  Temporal separation is enforced by schedule tables for TT traffic and bandwidth allocation for RC traffic
We proposed a timing analysis for the TTEthernet protocol
  Compared to other analyses, our analysis is much closer to the exact worst-case end-to-end delay, while requiring more time to obtain a result
Future work:
  Optimize the analysis to reduce the computation time
  Provide a more formal complexity analysis
Notes: To make more concise!